## Slide 1: Gateway EMX Performance Review
Planned Ridership Projections
vs. Observed Performance

## Slide 2: What is “BRT” ?
BRT is a hybrid transit service that typically has the following characteristics:
  Bus system advantages of at-grade street operations and route design flexibility.
  More extensive stop infrastructure than a standard City bus route
  Service design that is capable of handling high traveler volumes efficiently in dense urban areas.
Eugene/Springfield MSA population ranked 29th out of 30 and 22nd out of 30 in population density for U.S. communities with BRT

## Slide 3: Performance Review Objectives
Quantify the Gateway EMX operational performance through ridership counts
Compare observed ridership to the planning documents’ projected ridership
Collect Gateway EMX qualitative data for a generalized quality assessment
Assess the Overall Performance of the Gateway EMX Project

## Slide 4: Methodology
Literature and Policy Review
Peak Period Onboard Ridership Counts
Full Day Transit Stop Ridership Counts
Qualitative Field Data Collection of Notes and Observations by Principal Investigator
Data Analysis
Compare manual count analysis to APC data
Identify Analysis & Data Limitations/ Additional Research Opportunities
Conclusions

## Slide 5: Transit Stop Utilization Results
Sacred Heart Station Ridership was counted 89% to 83% below the 2025 EA projected ridership1
Centennial Station Ridership was counted 62% to 36% below the 2025 EA projected ridership1
1EA stands for Environmental Assessment which was the National Environmental Policy Act (NEPA) document that was the planning document used to justify the Gateway EMX project

## Slide 6: Peak Period Capacity Utilization
The planned BRT capacity utilization rate in the EA was only 20.5% by 2030
Onboard Peak Hour Counts were taken on April 14, 2015
The counted busses in the Gateway EMX had utilization rates below 7%
The utilization rates for the Gateway EMX were 66.2% below the EA 2030 projection

## Slide 7: Automated Passenger Counts
Primary limitation of the original analysis was sample size for the manual count data
APC data has its own limitations, but is a good comparative data set. LTD provided average boardings and alightings for October 2015.
The APC data showed modestly better performance than the manual count data:
  Sacred Heart Station Ridership was counted 89% to 84% below the 2025 EA projected ridership
  Centennial Station Ridership was counted 48% to 12% below the 2025 EA projected ridership

## Slide 8: APC Data Utilization Analysis

## Slide 9: Qualitative Assessment
Gateway EMX Appears Convenient and Reliable
Attractive Stop Architecture and Bus designs
Appears to be operated in a safe and conscientious manner
Stations are clean
Payment system is convenient and intuitive
Tight stop spacing on the loop portion of the route combined with low ridership does not impart a sense of “rapid” service

## Slide 10: Conclusions
Original EA utilization rate projection of 20.5% was deemed to be “Efficient”
Observed use of the Gateway EMX route appears to be two thirds or more below planned projections
At 13mph average, the Gateway EMX is not rapid service. Other standard bus routes in the LTD system operate at similar speeds

## Slide 11: Conclusions
Increased land development in the corridor may increase ridership over time but it appears insufficient to achieve the original ridership projections, - most likely by a significant margin
The Gateway EMX’s light usage was in sharp contrast to the Franklin EMX which was observed to be much more intensive and consistent with the academic literature for BRT operations

## Slide 12: Questions for the Future
Are other LTD transit services being curtailed in order to continue to run the Gateway EMX at current operational levels or are additional tax revenues being sought to avoid curtailment?
What changes to the service might be possible to maintain a high quality service but move in the direction of attaining originally projected utilization rates?